Assembly Language and Computer Architecture Lab
# Week 4
## Assignment 2
### abs $s0, $s1
If $s0 < 0:
- Shift all bit to the right arithmetically we get 32 bits 1 (0xffffffff)
- Using XOR for 0xffffffff and $s0 to get the 1’s complement number of $s0.
- Using subu to subtract 0xffffffff (which is -1) from the 1’s complement number, it means +1 to get the 2’s complement number.
If $s0 ≥ 0:
- Shift all bit to the right arithmetically we get 32 bits 0 (0x00000000)
- Using XOR for 0x00000000 and $s0 makes $s0 remains unchanged.
- Using subu to subtract 0x00000000 (which is 0) from $s0, also keeps $s0 unchanged.
### b) move $s0, $s1
Get sum of $zero and $s1, then store the result to $s0
### c) not $s0
Apply logic NOR to each bit of number in $s0 and bit 0 (taken from $zero) to reverse all bits.
### d) ble $s1, $s2, L
- First compare if $s2 < $s1 then $t1 = 1, if not then $t1 = 0
- Using beq to check if $t1=0, which means $s2 < $s1 is false, or $s1 ≤ $s2, then jumps to the branch. Otherwise, do not jump.